## Temperature Control Circuit with Selectable Levels
### 1. Objective
To design an electronic circuit capable of maintaining one of four selectable temperature levels (50 °C, 75 °C, 100 °C, 125 °C) with an accuracy of ±10 °C.
The circuit must be based on discrete components only (no microcontroller) and include an LED indicator for the heating process.
### 2. Circuit Components
Ref.	Component	Description
U1	LM7805	5 V voltage regulator for the control circuit.
U2A	LM393	Comparator for comparing temperature signal and reference voltage.
Q2	2N3055 (NPN)	Power transistor to drive the heater (to 60V 15A).
R1	10 kΩ	Fixed resistor forming a divider with the PT1000 sensor.
PT1000	Platinum RTD sensor	Measures temperature (≈1000 Ω at 0 °C).
R2	10 kΩ	Pull-up resistor for the comparator output.
R3–R7	12 kΩ, 13 kΩ, 14 kΩ, 15 kΩ	Voltage divider resistors for selectable reference voltages.
SW1	DIP switch ×4	Selects one of four temperature levels.
R6	330 Ω	Current-limiting resistor for the LED.
D1	LED	Indicates heater activation.
J1	Power connector	12 V input for the circuit.
J3	Output connector	Connection to external heater.

### 3. Operating Principle
1. LM7805 provides a regulated 5 V supply for the control circuitry.
2. PT1000 and R1 = 10 kΩ form a voltage divider:
  Vtemp​=5×RPT1000​+R1 / RPT1000​​
3. The sensor voltage varies with temperature as follows:
Temperature (°C)	R_PT1000 (Ω)	V_temp (V)
50	1190	2.72
75	1285	2.81
100	1380	2.90
125	1476	2.98

The reference voltage is generated by the resistor network R3–R7 and the DIP switch.
The voltage is calculated as:
Vref​=5×R1​+R2​R2​​
Using R1 = 10 kΩ, the corresponding resistor values for each temperature are:
Temperature (°C)	V_ref (V)	R2 (calculated)	Used value
50	2.72	11.9 kΩ	12 kΩ
75	2.81	12.7 kΩ	13 kΩ
100	2.90	13.8 kΩ	14 kΩ
125	2.98	14.8 kΩ	15 kΩ

1. The LM393 comparator compares:
  1. V+ → reference voltage from the DIP switch
  2. V– → signal from the PT1000 divider
  When the temperature is below the selected level (V– < V+), the comparator output goes low, turning on the transistor 2N3055, which drives the heater and illuminates the LED.
### 4. Calculations
1️. Sensor voltage divider:
Vtemp​=Vcc ​× Rpt1000 / (R1 + Rpt1000)
2️. Reference divider resistor:
R2​ = R1​ × Vref / (Vcc - Vref)
3️. Base current for transistor:
IB = Iload / hfe = 2A/50 = 40mA
Comparator output current ≈ 5 V / 330 Ω = 15 mA → sufficient to drive 2N3055 through R6 = 330 Ω.
### 5. Conclusions
- The circuit maintains four selectable temperature levels: 50 °C, 75 °C, 100 °C, 125 °C.
- Accuracy of ±10 °C is achieved using a stable 5 V reference (LM7805) and a precision PT1000 sensor.
- The LED provides visual feedback during heating.
- The design uses only discrete components, with no microcontroller.
- The power stage (2N3055) allows for heater control up to 60V / 15A